## Slide 1: Embedded Linux Development
Getting Started with the Raspberry Pi 4 Embedded Board

## Slide 2: Outline
Introduction to Embedded Operating Systems
  Taking off from where we left
  Host, Target, Developmen Env, Debug Env and Operating Systems
The Linux Embedded System
  The Basics - Tool chains, libraries, debuggers
  The Board Support Package - Boot Loader, Kernel and File System
Introduction to Raspberry Pi4

## Slide 3: Classifications of Embedded Systems
Owing to Memory Size & Power Consumption
  Small ES - Low Power CPU, < 4MB ROM (Flash) and 8-16MB RAM
  Medium ES- Med Power CPU, 32MB+ ROM and 64-128MB RAM with optional Secondary Storage
  Large ES - High Power CPU, Large Memory Banks...
Owing to Timing Constraints
  Stringent Deadlines - Hard and Soft Realtime
  Mild Deadlines - Timing is not a major issue
Networkability
User Experience

## Slide 4: Classification of Embedded Systems Programming
Bare Metal Programming
Hardware
User Application + Embedded OS / RTOS
Hardware
User Space
Hardware
OS / Kernel Space
Software
Hardware
Hardwired Systems
Two-Tiered Architecture
Three-Tiered Architecture

## Slide 5: High End Embedded Systems – Components of the Board Development Environment
Software Terminologies
  Toolchain - Set of executables that are required to compile and build an embedded systems image
  Boot Loader – Piece of code which is required to load the Kernel and subsequent OS related software
  Kernel - Part of the Operating System that provides its features and services
  Root File System –
    Software that abstracts the low-level hardware details and presents a logical file storage and access interface.
    Contains all the files of the Operating System with a mechanism and programs to access them
    Applications are developed and reside in the RFS and are accessed using various tools provided by the OS
  Libraries – Pieces of code that implement specific functionality which can be used by other software
Build System
  One on which the toolchain is built
Host Device
  Any device capable of performing cross platform development
  Linux Workstation, Unix System and Windows
  Build the programs and create the object file, which will be executed on the target device
Target Device
  The device onto which developed software has to be flashed and executed
  X86, ARM, PowerPC, MIPS processor etc

## Slide 6: A Typical Embedded System Environment – Linked Setup
Kernel
Root Filesystem
Cross Platform Development Environment / Toolchains
Build & Host Device
Target Device
Bootloader
Kernel
Root Filesystem

## Slide 7: Development Configurations - Removable Storage Setup
Cross Platform Development Environment
Secondary Bootloader
Kernel
Root Filesystem
Bootloader
Build & Host Device
Target Device

## Slide 8: Development Configurations - Standalone Setup
Bootloader
Kernel
Full Root Filesystem
Native Development Environment

## Slide 9
The Embedded Linux Software Eco System
Build System for Linux Development
Toolchain
Board Support Package
Integrated Development Environment
Test Environment
Simulation/ Emulation Setup
Application Development Support
Target Hardware
Programming Flashing
Debug Environment
Compiler, Binary Utilities, Libraries
Boot Loader, Kernel,
Root File System

## Slide 10: The Toolchain
“Building a [ … ] cross-toolchain for use in embedded systems development [ is ] a scary prospect, requiring iron will, days if not weeks of effort, lots of Unix and Gnu lore, and sometimes willingness to take dodgy shortcuts.”
-Dan Kegel, the main author of Crosstool

## Slide 11: Toolchain
Compiler
Cross Compiler & Cross-Native Compiler
Binutils
Assembler & Linker, Profiler & Coverage
Debugger
Kernel & Application Debugger
Tracing Analysis
Object Copy & Object Dump
Programmer
Flash programming
Linux Compiler & Embedded C Compiler
Library
Secondary Storage Setup & Removable Storage Setup
Linux Kernel Headers
C- Runtime Libraries: Glibc & uCLibC

## Slide 12: Toolchain: 1. Compiler
Native Compiler
Cross Compiler
Cross-Native Compiler
X86/Linux OS
Build System
X86/Linux OS
Host System
X86/Linux OS
Target System
Build System - The system on which the compiler is compiled
Host System - The system on which the compiler is executed
Target System - The system for which the compiler generates the executable and the system on which executable runs
X86/Linux OS
Build System
X86/LinuxOS
Host System
ARM
Target System
X86/Linux OS
Build System
ARM
Host System
ARM
Target System

## Slide 13: Compiler
Cross Compiler
  The cross compiler is generated by compiling the compiler source code (gcc) for a target platform (eg. ARM) using the native compiler of the build system
    Eg: Native gcc of x86 platform is used to compile the gcc for arm-linux, setting the target to be arm architecture
  The cross-compiler executes on the host system, but generates the executable which can be run only on the target platform
    Eg: arm-linaro-linux-gnu-gcc –o hello hello.c
  Generated executable will execute on the target platform only
  Usage
    Required to compile the Bootloader, Kernel and other drivers, required for boot process of the target board

## Slide 14: Compiler
Cross-Native Compiler
  This compiler is compiled on the build system, using the cross compiler of the target
  Generates an executable for the target platform, which is the native compiler for the target
  Executes on the target platform and is used to generate executables on the target platform, for the target platform
  Here, the host platform and the target platform remain the same
  Usage
    Included into the Root File System of the target platform and can be used directly on the board
    Used to compile applications on the target platform

## Slide 15: The Compiler (ARM-LINUX-GCC)
ARM-GNU Compiler Collection
  Contains the program to understand the grammar of a language and generate the object file specific to a particular hardware platforms
Native Compiler and Cross Compiler
Pre-built or Sources
Popular Compiler Distributors for ARM
  Linaro - https://releases.linaro.org/14.04/components/toolchain/binaries/
  CodeSoucery - https://www.mentor.com/embedded-software/sourcery-tools/sourcery-codebench/overview
  Crosstool-ng - http://crosstool-ng.org/download/crosstool-ng/
  Musl-cross - https://bitbucket.org/GregorR/musl-cross
Application Binary Interface (ABI)
  Allows portability across binaries generated by various toolchain vendors

## Slide 16: Toolchain: 2. Binutils
Utility | Use
as | GNU assembler
ld | GNU linker
gasp | GNU assembler pre-processor
nm | Lists the symbols in an object file
objcopy | Copies and translates object files
objdump | Displays information about the content of object files
ranlib | Generates an index to the content of an archive
readelf | Displays information about an ELF format object file
size | Lists the sizes of sections within an object file
ar | Creates and manipulates archive content
Source: https://www.gnu.org/software/binutils/
Latest Stable Version: 2.30

## Slide 17: Toolchains: Binutils
Use Cases
  If binutils is to be used to generate executables for the target platform
    The binutils are to be compiled with the native compiler of the host, specifying the appropriate target
  If binutils is to be used in the target platform,
    It should be compiled using the cross compiler of the target and shipped with the rootfs of the target

## Slide 18: Creating the Build Environment
Compiler
  Use pre-built compiler (or)
  Compile the compiler, debugger and binary utilities using native compiler and configurations
Libraries
  Compile the libraries in the presence of its headers and create the images, using cross compiler
Debugger
  Compile the debugger
Environment
  Set the environment for development
Build the toolchain which will be used to build other components for the board support package. This will execute on the host system
Use the Cross Tool Chain to build components that will run on the Target Device. These components will be loaded in the Root File System
CN Compiler
Bin-utils
Bin-utils
Debugger
Libraries
Compiler
Bin-utils
Debugger
Libraries
Headers

## Slide 19: Toolchains: 3. Libraries

## Slide 20: Toolchains: 3. Libraries
GNU C Library (glibC)
  Source - https://www.gnu.org/software/libc/
  Current Stable Version: 2.24
  Portable, Extensive, High Performance
  Supports ISO C99, POSIX 1.c, 1.j and 1.d, UNIX 98
  Good for Host Systems, but falls short in Embedded Systems owing to large size. Minimum size is 2MB
  Optimized for performance and not memory…
uCLibC
  Small C Standard Library for Linux Kernel based Embedded Systems
  Free and Open Source, complying to LGPL library
  Light Weight supporting MMU-Less Linux
  Supports number of hardware platforms
  Source - https://uclibc.org/
  Current Stable Version: 0.9.33.2

## Slide 21: Toolchains: Headers
Required to compile the Library and User Applications for specific kernels
Sanitized Headers
  Post 2.6 version of kernel, a sanitized version of the headers is generated for tool chain and application usage. This differs from the kernel headers, which contain inline assembly code, compromising the kernel, if used in application code

## Slide 22: Debugger – Target-in-line
Eclipse Based IDE
GDB Client + Insight
Open OCD running GDB Server with support for ARM
CPU Core
Target ARM Board
Host Device
Debug Adapter
USB
Serial
Ethernet
JTAG Core
JTAG Signals
GDB Console
USB/Serial

## Slide 23: Debugger – External
Target-in-line Debugging
  Source level debugging of Linux Kernel & Bootloader
  Support for debugging of dynamic modules
  Integrates gdb with OpenOCD on the host, allowing the user to debug a remote target through a JTAG adapter
  OpenOCD is supported by ARM architectures
  Configuration scripts for CPU core and board should be developed for Open OCD to be used
  Debug support for peripherals on the core and peripherals on the board may be architected as part of the design

## Slide 24: Debugger – Internal
Application Debugging
  User space application may be debugged using the gdb client server model, running on the target board
  Native debugger (gdb) for the ARM architecture is required to perform the debug
  Added into the Root File System of the target platform

## Slide 25: Debugger – Linux Trace Toolkit
Host System
Eclipse Based IDE
Trace Analysis Software
Target Board
Linux Kernel Patched with Trace Support
Trace - Kernel Module
VFS
Trace Daemon
USB/Serial

## Slide 26: Debugger
Linux Trace Toolkit
  Includes kernel components and user-level tools required to view traces
    Linux Kernel patched with trace support
    Linux Kernel module which collects trace events
    Trace Daemon that receives the trace events from the linux kernel and stores it into the Filesystem
    Trace analysis tool that can be run on a remote system (host) for analysis
  Trace support should be integrated with the kernel as part of project

## Slide 27: The Board Support Package

## Slide 28: Board Support Package Development
Boot loader
Uboot, Redboot, GRUB
Linux Kernel
Port Code Development & Porting to target platform
Device Tree Sources for Core and Board
Peripheral Drivers
Peripherals internal and external to the core
Multicore support
Interrupt Management
Networking Stacks
Boot Architecture - BIOS -> Level 1 Bootloader -> Level 2 Bootloader
Peripheral Driver support for booting
Root File System
Creating and populating the RFS
uCLibc/glibc
Utilities for development (Busybox) & Init Process for user space

## Slide 29: Building the Sources
Toolchain Environment
Bootloader
Kernel
Root File System
Compile
Compile
Populate
Prepare the environment for booting the kernel
Transfer control to the kernel
Boot the system and Load the Root Filesystem
boot
bin
lib
home

## Slide 30: The Bootloader
RESET
Bootloader valid in flash?
Application valid in Flash
Wait for new app from host
Timeout
Host Communication Start?
Wait Indefinitely?
Host Communication Start?
HALT
Receive New Application from Host. Overwrite Existing
Load Application
NO
NO
NO
NO
NO
NO
NO
YES
YES
YES
YES
YES
YES
YES
START

## Slide 31: The Bootloader - GNU Grand Unified Bootloader (GRUB)
Developed by Free Software Foundation
Provides Multi-boot facility to load multiple operating systems
Highly configurable through bash-like command line interface
Supports almost all filesystem types
Two Stage Loading
Ref: https://www.gnu.org/software/grub/
Supports Ethernet, USB and SATA based loading of the kernel

## Slide 32: The Bootloader - uboot
Multi-platform, open-source, universal boot-loader with comprehensive support for loading and managing boot images, such as the Linux kernel
Features
  Network download: TFTP, BOOTP, DHCP, NFS
  Serial download: s-record, binary (via Kermit)
  Flash management: copy, erase, protect, cramfs, jffs2
  Flash Types: CFI NOR-Flash, NAND-Flash
  Memory utilities: copy, dump. crc, check, mtest
  Mass Storage Devices: IDE, SATA, USB
  Boot from disk: raw block, ext2, fat, reiserfs
  Interactive shell: choice of simple or "busybox" shell with many scripting features
Powerful Commandline Interface via Serial Port
Ref: https://sourceforge.net/projects/uboot/

## Slide 33: The Linux Kernel…
Contains the Operating System code and low level drivers/modules to interact with hardware and provide services to the user….
Latest Stable Version is 5.9.6
Ref: www.kernel.org

## Slide 34: The Linux Operating System Architecture

## Slide 35: The Linux Kernel Architecture

## Slide 36: The Rootfilesystems
Contains the applications, services, libraries and other executables that a user may require to run his applications.
Created with a specific filesystem type – ext2,3,4, fat32, squash, flashfs, etc
Loaded by the kernel for user applications to proceed
All libraries and native tools for further build are stored in the rootfilesystem

## Slide 37: Embedded Systems – Board Development Environment
Build System
  One on which the toolchain is built
Host Device
  Any device capable of performing cross platform development
  Linux Workstation, Unix System and Windows
  Build the programs and create the object file, which will be executed on the target device
Target Device
  The device onto which developed software has to be flashed and executed
  X86, ARM, PowerPC, MIPS processor etc
Development Configurations
  Linked Setup
  Removable Storage Setup
  Standalone Setup

## Slide 38: Pre-requisites to get an embedded board running Linux
Tool Chain – Set of software tools needed to build computer software
  Compiler
    Native– Compiled on one architecture and runs on the same architecture (gcc for x86)
    Cross Toolchain– Compiled on one architecture, runs on that architecture and builds code for another architecture (arm-linux-gcc)
    Cross Native Toolchain – Compiled on one architecture, runs on a target architecture and builds code for the target architecture
  Library: Glibc, uClibc, newlibC
  Headers: For Prototype declarations and resolving
  Bin-utils: Linker, Assembler, Object File Interpreters (objcopy, objdump), etc…
  Debugger: gdb
Bootloader
  Grub, uboot, redboot,
Kernel
  Requires platform specific port code and configurations
  Sometimes, Board to platform bindings are also required
Root Filesystem

## Slide 39: Thanks

## Slide 40: The Raspberry Pi4

## Slide 41: Raspberry Pi4
Tech Specs
Broadcom BCM2711, Quad core Cortex-A72 (ARM v8) 64-bit SoC @ 1.5GHz
2GB LPDDR4-3200 SDRAM
2.4 GHz and 5.0 GHz IEEE 802.11ac wireless, Bluetooth 5.0, BLE
Gigabit Ethernet
2 USB 3.0 ports; 2 USB 2.0 ports.
Raspberry Pi standard 40 pin GPIO header (fully backwards compatible with previous boards)
2 × micro-HDMI ports (up to 4kp60 supported)
OpenGL ES 3.0 graphics
Micro-SD card slot for loading operating system and data storage
5V DC via USB-C connector /GPIO header (minimum 3A*)
Power over Ethernet (PoE) enabled

## Slide 42: GPIO Available

## Slide 43: OFF TO DEVELOPMENT
Create the SD Card Image for the Raspberry Pi4 Board
  Download the SD Card image from your FTP – It is stored by the name Rpi.img
  This image has to be flashed onto the SD Card before booting the Pi
  Insert the SD card into the SD card Reader
  Unmout the SD Card Reader: sudo umount /media/<check the name of the card>
  Transfer the image to the SD card: dd if=Rpi.img of=/dev/sdb bs=4M. This will take about 40 mins.
  Once completed, insert the SD card into the board. Follow the notes mentioned here and start programming
Creating the Cross Development Environment
  Download the folder DeviceDrivers.zip from FTP
  Unzip the folder into your home directory – unzip DeviceDrivers.zip
  Change Directory to DeviceDrivers
  Follow instructions in the install-Rpi.txt to install the Cross Development Environment
NOTES
  Default IP on the Raspberry Pi4 is set to: 192.168.0.10
  Set your PC to 192.168.0.2 using the following command: sudo ip addr add 192.168.0.2/24 dev <iface name>
  Connect to the Board by executing the following on the terminal: ssh –X pi@192.168.0.10 . Password is cdac@123
  Start Your Programs in DD-Progs Folder.

## Slide 45: Toolchain References
Linux From Scratch project (http://trac.cross-lfs.org)

## Slide 46: Debug Options
Serial Interface
  UART/USB
Network Interface
  Ethernet Protocols
Debugging Hardware
  JTAG

## Slide 47: Buildroot

## Slide 48: Open Embedded and Yocto Project

## Slide 49: Device Tree Sources…